Instruction Manual for Toroidal Coil

Product No.：TM3201

- Description

The product is twined by multiple turns of copper wire. The terminals are installed on the holder so that experiment will be easy to operate. It is mainly used to explore electromagnetic induction. The product structure is easy, solid and durable.

- Product Specification

| NO. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Toroidal coil |  | 1 piece |  |

Tab.1

- Product General Assembly Figure

Fig.1

- Product General Assembly Procedures

Assembly is not required as shown in Fig.1.

- Notes

1. The maximum current should not exceed 3A.

2. Try not to fall the toroidal coil otherwise it may not work properly.

3. Check if toroidal coil is conducting before using.

4. Try to keep all the objects which works dependent on magnetic away from toroidal coil.

- Maintenance

1. Horizontally place it in dry and dark place.

2. Handle it carefully.

3. Clean stains on the surface after using.

4. Solder the copper wire using soldering iron if it falls off.