Instruction Manual for Solenoid

Product No.：TM3202

- Description

The product is twined by multiple turns of copper wire. It is covered by lucency acrylic tube in order to protect the wires. The terminals are installed at end of holder so that experiment will be easy to operate. It is used to explore the uniform magnetic field generated in solenoid.

- Product Specification

| NO. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Solenoid |  | 1 piece | Resistance is around 21Ω |

Tab.1

- Product General Assembly Figure

Fig.1

- Product General Assembly Procedures

Assembly is not required as shown in Fig.1.

- Usage

Connect student power supply to terminals on solenoid using wires. Place the magnetic induction intensity sensor probe along the axis of solenoid at 5cm away from the end. Move the probe into solenoid along the axis. The existence and changing of uniform magnetic field can be measured by datalogging and experiment software.

- Notes

1. Solenoid should not be conducting for long time. The maximum current should not exceed 1A.

2. Try not to fall the solenoid otherwise it may not work properly.

3. Check if solenoid is conducting before using.

4. Try to keep all the objects which works dependent on magnetic away from solenoid .

- Maintenance

1. Horizontally place it in dry and dark place.

2. Handle it carefully.

3. Clean stains on the surface after using.

4. Solder the copper wire using soldering iron if it falls off.