Instruction Manual for Photosynthesis Experiment Chamber

Product No.: TP2018

- Description

This product consists of chamber, seal cover, and rubber stoppers. It can be used to demonstrate plant photosynthesis, respiration, germination of seed, transpiration, candle and simulated ecosystem.

- Product Specification

| No. | Name | ID | Picture | Parameter | Quantity | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Chamber, seal cover |  |  |  | 1 set |  |
| 2 | Fully-enclosed rubber stopper (side of cover) | B0 |  | Φ30 | 2 pieces | Used to seal the side hole |
| 3 | Fully-enclosed rubber stopper (top of cover) | A0 |  | Φ33 | 3 pieces | Used to seal the top hole |
| 4 | Nonporous stopper with a benching | A1-I |  | No.7 stopper, grooved 4mm | 2 pieces | Used for top hole, to fix pH, conductivity, DO, dissolved carbon dioxide, salinity, temperature, DO-O2 sensors and sensor probe cable |
| 5 | Nonporous stopper with two benching | A1-II |  | No.7 stopper, grooved 4mm | 3 pieces | Used for top hole, to fix pH, conductivity, DO, dissolved carbon dioxide, salinity, temperature, DO-O2 sensors and sensor probe cable |
| 6 | Stopper for temperature probe | A2 |  | Φ33, Mesopore 4mm | 1 piece | Used for top hole, to insert the temperature probe |
| 7 | Stopper for O2 probe | A3 |  | Φ33, Mesopore 18mm | 1 piece | Used for top hole, to insert the O2 probe |
| 8 | Stopper for CO2 probe | A4 |  | Φ33, Mesopore 15mm | 1 piece | Used for top hole, to insert the CO2 probe |
| 9 | Stopper for humidity | A5 |  | Φ33, Mesopore 14mm | 1 piece | Used for top hole, to insert the humidity probe |
| 10 | Stopper for DO-O2 probe | A6 |  | Φ33, Mesopore 12mm | 1 piece | Used for top hole, to insert the DO-O2 probe |

Tab. 1

- Product General Assembly Figure

Fig.1

- Product Assembly Procedures

Assembly is not required as shown in Fig.1.

- Typical Experiments

Factors that affect the rate of photosynthesis: CO2 concentration

Factors that affect the plant photosynthesis: illumination

Plant transpiration

Exothermic of Seed germination

Respiration of Yeast

- Notes

1. The quality of water all over the world is different. If there is some white precipitate after adding the sodium bicarbonate. Please use the distilled water.

2. In the photosynthesis of aquatic plants experiment, cut the young branches from the fresh aquatic green plants. Put the pruning wound to face upside. The optimum water temperature range is 20℃-25℃.

3. Provide enough illumination when doing the photosynthesis of aquatic plants experiment. Add some artificial light if necessary.

4. The interface crack can be fixed by using the chloroform (hydrogen imitation).

5. If there is gas leaking, it can be solved by smearing vaseline at the joint.

- Maintenance

The device should be placed in a cardboard box if not in use. Use a damp cloth to wipe out the dust on the surface lightly. Avoid scratches caused by sharp articles on the surface.