Instruction Manual for Boyle’s Law Demonstrator

Product No.: TP2025

# Description

The demonstrator consists of holder, piston holder and syringe. It is used to explore the relationship between pressure and volume changing for a certain quantity of gas at constant temperature. Thus, the Boyle's law can be explored. The demonstrator is practical and reliable.

# Product Specification

| No. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Boyle’s law demonstrator |  | 1 set | Include holder, piston holder and syringe |

Tab. 1

# Product General Assembly Figure

Fig. 1: Boyle’s Law Demonstrator

# Product General Assembly Procedures

Assembly is not required, as shown in Fig. 1.

# Notes

1. Cover the nozzle of syringe using hose of the absolute pressure sensor. Make sure that it is sealed and no gas leaking before the experiment.

2. The adjustable range of piston is between 20mL to 60mL.

# Maintenance

The device should be placed in a cardboard box if not in use. Use a damp cloth to wipe out the dust on the surface lightly. Avoid scratches caused by sharp articles on the surface.