Instruction Manual for Water Solidifying & Ice Melting Demonstrator

Product No.:TP2030

- Description

The product consists of ice maker, water tank and 12V 8A adapter. It is used to observe the water solidifying and ice melting phenomena and analyzing its regulation.

- Product Specification

| No. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Ice maker |  | 1 piece | Including radiator |
| 2 | Small bottle with stopper |  | 1 piece | Transparent bottle diameter: 12mm |
| 3 | Water tank |  | 1 piece | Transparent plastic water tank |
| 4 | Power adapter |  | 1 piece | 12V 8A |
| 5 | Syringe with hose |  | 1 piece | 20ml syringe |

Tab.1

- Product General Assembly Figure

Fig.1

- Product General Assembly Procedure

Assembly is not required, as shown in Fig. 1.

- Notes

1. Inject the water into the water trough through the small hole on the panel by using the syringe before experiment. Make sure the water level is kept 5mm~10mm lower than the top of water tank.

2. The volume of water should be kept not more than half of the bottle.

- Maintenance

The device should be placed in a cardboard box if not in use. Use a damp cloth to wipe out the dust on the surface lightly. Avoid scratches caused by sharp articles on the surface.