Instructional Manual for Labor Saving on the Slope Experimental Equipment

Product No：TP4014

- Product introduction

This product consists of control parts, trolley, power adapter and USB cable. It is used to explore the relationship between the size of tension force and inclination angle of slope.This product is designed to meet the teaching requirements, easy to operate and practical.

- Product Specification

| No. | Component names | Sample picture | Quantity | Notes |
| --- | --- | --- | --- | --- |
| 1 | Iron stand part |  | 1 | 800mm |
| 2 | control part |  | 1 | Length, width and height: 710x104x78mm (including fishing line, lobster clasp) |
| 3 | trolley |  | 1 | The length, width and height are 105x60x65mm (about 388g) respectively. |
| 4 | power adapter |  | 1 | DC12v500mA |
| 5 | USB cable |  | 1 | 106x60x77mm |
| 6 | Bluetooth adapter |  | 1 |  |

Tab. 1

- Product General Assembly Figure

Fig.1

- General Assembly Procedures

- Fasten the iron stand with nuts.

- Tighten the control part on the iron stand as a whole.

- Connect the control part to the trolley with fishing line and lobster clasp, so that the control part can drag  the trolley to move.

- Notes

- When using, connect the power adapter to the control part first, then connect the circuit, pay attention to the electricity safety.

- When using the track, pay attention to safety, avoid being scratched by the sharp part of the track.

- When the inclination angle of slope is large, pay attention to tightening the nut to avoid the slide of inclined plane.

- Specific experimental methods can refer to the latest version of the experimental instruction manual.

- If the trolley cannot stop normally due to changes in environmental conditions (light intensity), the stopping distance of the trolley's forward rotation shall be set.

Steps:

- Put the trolley in the expected stop position of forward rotation (within 3cm from the control unit).

- Press and hold the stop button, and then press the reverse button. The red indicator on the controller starts to blink. At the same time, release it. Red indicator lights stop flashing, set complete.

- If the red indicator does not stop flashing, the position of the trolley shall be adjusted to keep close to the control part until the red indicator stops flashing and the setting is completed.

- Risk Warning

- It can seriously reduce the service life of the equipment when using in damp, corrosive gas, high temperature and other harsh environment.

- Be sure to remove the charger within 4 hours after full charge, so as not to affect the battery life.

- When the equipment power is low, please charge in time to avoid long time in low battery status.

- In case of any failure, please contact our company immediately. Do not disassemble the battery, disassemble the battery and use the sharp tool to penetrate the battery.

- When the temperature rise or other suspicious phenomenon is found in the use of electrical equipment, the power outage will be stopped immediately.

- If the equipment is not used for a long time, it must be guaranteed to be charged every 3 months or so.

- Maintenance

- When not in use, the equipment should be placed in the carton box, and clean the surface dust with a dry cloth wipe.

- When using the track, handle it lightly to avoid the damage of the track surface caused by collision with other objects.

- After the trolley is used, turn off its Bluetooth switch in time to avoid power loss.

# Text boxes

Iron stand

Trolley

control part