Instruction Manual for Law of Resistance Demonstrator II

Product No.：TP6003

- Description

The product consists of acrylic base, 4mm socket hook (red) and five metal wire. It is mainly used to explore the law of resistance and the factors affect resistance. The diameter of each string is: nickel chrome wire (0.2mm), nickel chrome wire (0.4mm), nickel chrome wire (0.6mm), Constantan wire (0.6mm) and Chromium iron wire (0.6mm).

- Product Specification

| No. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Law of resistance demonstrator II |  | 1 piece |  |
| 2 | 4mm socket hook |  | 1 pair |  |

Tab.1

- Product General Assembly Figure

Fig.1

- Product General Assembly Procedure

Assembly is not required.

- Experimental Case

Explore factors affect resistance.

- Notes

1. Make sure the circuit is connected properly. Keep the switch open before experiment. Keep the 	sliding rheostat at the maximal resistance level when the circuit is connected.

2. Open the circuit before changing the conducting wire.

3. It is recommended that complete the experiment as quick as possible.

4. The maximum applied voltage should not exceed 3V. It is suggested to be 2V.

- Maintenance

The device should be placed in a cardboard box if not in use. Use a damp cloth to wipe out the dust on 	the surface lightly. Avoid scratches caused by sharp articles on the surface.