Instruction Manual for Apparatus for Water Boiling

Product No.：TP6027

- Description

The product consists of iron stand, stainless steel alcohol lamp, 250ml beaker holder, asbestosed wire gauze, 250ml beaker, rotary union, temperature sensor holder, hand screw and cardboard cover. It is used to explore temperature and bubble rising change before and after water boiling. The product is practical and easy to operate.

- Product Specification

| No. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Iron stand |  | 1 set | Length: 600mm |
| 2 | Stainless steel alcohol lamp |  | 1 set | Diameter: Φ75 Height: 120 |
| 3 | Beaker holder |  | 1 set | Diameter: Φ100 Length: 120 |
| 4 | Asbestosed wire gauze |  | 1 piece | 145×145×1.5 |
| 5 | 250ml beaker |  | 1 piece | Φ75×95 |
| 6 | Rotary union |  | 1 set |  |
| 7 | Temperature sensor probe holder |  | 1 piece | Φ16×180 |
| 8 | Hand screw |  | 2 pieces | M4×12 |
| 9 | Cardboard cover |  | 10 pieces | 105×148mm |

Tab.1

- Product General Assembly Figure

Fig.1

- Product General Assembly Procedure

Assembly is not required, as shown in fig.1.

- Experimental Case

Explore water boiling

Experiment name

Explore water boiling

Experimental aim

To explore temperature and bubble rising change before and after water boiling.

Experimental principle

Water boiling is a drastic vaporization. Temperature change when water gets heated. Temperature sensor is used to measure the temperature change when water absorbs heat and observe bubble change before and after water boiling during the experiment.

Experimental apparatus

Computer, apparatus for water boiling, SenseDisc and temperature sensor.

Experimental installation figure

Fig.2: Product General Assembly

Experimental procedures

Preparation:

- Install the apparatus according to Fig.2. Connect temperature sensor to SenseDisc.

- Mount temperature sensor probe and open experiment software.

- Select  to open experiment menu.

- Select  at top right corner.

- Click  in the experiment menu to create experiment template.

- Click  at right top corner to read experiment guide.

- Set proper time interval such as 1s and 2s.

Experiment:

Use hot water to heat. Light up alcohol lamp. Click ‘Start’ and temperature will change. The table will display data and points are shown in coordinate only when temperature reaches 0℃. You can observe bubble change before and after boiling. Click ‘Stop’ after experiment. Click ‘fit’ to collect all data points in the figure. Observe and analyze the experimental result. Click ‘Start’ to record data if you need to restart experiment.

Fig.3: Experimental Result

- Notes

1. The beaker holder and asbestosed wire gauze will become extremely hot because of alcohol lamp. Be careful.

- Operating System

| Connection | Support wire and wireless connection. |
| --- | --- |
| Supported system | Windows xp and above, iOS 8.0 and above, android 2.0 and above. |

- Maintenance

The device should be placed in a cardboard box if not in use. Use a damp cloth to wipe out the dust 	on 	the surface lightly. Avoid scratches caused by sharp articles on the surface.

# Text boxes

Beaker holder

Temperature sensor probe holder

Asbestosed wire gauze

Rotary union

Iron stand

Beaker

Stainless steel alcohol lamp