Instruction Manual for Apparatus for Internal Pressure of Liquids

Product No.：TP6032

- Description

The product consists of apparatus for internal pressure of liquids (including rubber band), water tank and sensor connector. It is used to explore internal pressure of liquid and factors affect it.

- Product Specification

| No. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Apparatus for internal pressure of liquids |  | 1 set | One apparatus for internal pressure of liquids. 3.2-6.4mm two-way valve joint. One piece of 0.2m silica gel tube. One piece of 0.4m silica gel tube. 6.4mm T-type three-way valve joint. |
| 2 | Water tank |  | 1 piece | Rectangular water tank (15*10*30cm) |
| 3 | Sensor connector |  |  | Transparent Luer connector 1/4. It is used to connect to sensors. |

Tab.1

- Product General Assembly Figure

Fig.1

- Product General Assembly Procedures

Setup the apparatus as shown in fig.1. Mount the apparatus in water tank. Connect silica gel tube to U-shape tube. Mount the sensor connector on the other end of silica gel tube.

- Notes

1. It is required to rotate the connector of silica gel tube to assembly or disassembly.

2. Be careful when install the rubber band because of strong elasticity.

3. Check the installation before experiment in case gas leaking.

4. Check if the sensor connector can be connected to sensors before experiment. Change sensor connector if it can not connect.

- Maintenance

The device should be placed in a cardboard box if not in use. Use a damp cloth to wipe out the dust on 	the surface lightly. Avoid scratches caused by sharp articles on the surface.