Instruction Manual for Apparatus for Boiling Point and Pressure

Product No.：TP6033

- Description

The product consists of iron stand, syringe kit, conical flask 250ml, beaker holder, asbestosed wire gauze, flask clamp, flask clamp holder, tube holder and alcohol lamp. It is used to explore temperature and bubble rising change before and after water boiling. The product is practical 	and easy to operate.

- Product Specification

| No. | Name | Picture | Quantity | Remark |
| --- | --- | --- | --- | --- |
| 1 | Syringe kit |  | 1 set | 4 pieces of 0.2m silica gel tubes 1 piece of 0.5m silica gel tube 1 piece of two-way valve joint 1 piece of straight joint 1 piece of 100ml syringe. 1 piece of copper joint 1 piece of one-way valve 1 piece of four-way valve joint 1 piece of 7# rubber stopper 1 piece of blue cover |
| 2 | Conical flask 250ml |  | 1 piece | 250ml glass triangle flask |
| 4 | Beaker holder |  | 1 set | Diameter：Φ100 Length: 120 |
| 5 | Asbestosed wire gauze |  | 1 piece |  |
| 6 | Flask clamp |  | 1 set | Single screw triple claws clamp |
| 7 | Flask clamp holder |  | 1 piece |  |
| 8 | Tube holder |  | 1 piece | 2 pieces of plastic clamp, 1 piece of holder and one wing screw |
| 9 | Alcohol lamp |  | 1 piece | Stainless steel ss-200-1 |

Tab.1

- Product General Assembly Figure

Fig.1

- Product General Assembly Procedure

Assembly is shown in fig.1.

- Notes

1. The beaker holder and asbestosed wire gauze will become extremely hot because of alcohol lamp. Be careful.

2. Tubes will be extremely hot during heating up. Be careful when you exhaust and inject.

- Maintenance

The device should be placed in a cardboard box if not in use. Use a damp cloth to wipe out the dust on the surface lightly. Avoid scratches caused by sharp articles on the surface.