Voltage Sensor

Voltage Sensor is used to measure the electric potential difference at both ends of the electrical equipment or circuits. Voltage Sensor divides the voltage it collects to measure the electrical potential difference in DC circuit and low-voltage, low-frequency AC circuit.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0001 | Voltage Sensor |  |
| 2 |  | Red alligator clip |  |
| 3 |  | Black alligator clip |  |

Usage

Connect Voltage Sensor to any port in SenseDisc.

Connect red and black alligator clips to positive and negative poles in current sensor.

Parallel connect Voltage Sensor into circuit.

Calibration

Voltage Sensor needs to be calibrated before using.

Short connect red and black alligator clips.

Open experiment software . Click  and select ‘Voltage Sensor’. Click ‘Calibrate’ ‘OK’ to complete calibration.

Typical experiment

Series and parallel connection of resistor

Solar power generation

Measure the VA characteristic curve of small bulb

LC oscillation

Ohm's Law

Notes

Voltage Sensor should be parallel connected to the circuit during using.

Voltage Sensor needs to be calibrated before using.

The maximum voltage can be applied to sensor is 250V.

# Text boxes

S0001 Voltage Sensor

Measuring range: -30~30V

Accuracy: ±1%

Resolution: 0.02V

Input impedance: 2MΩ