# Voltage Sensor

Voltage Sensor is used to measure the electric potential difference at both ends of the electrical equipment or circuits. Voltage Sensor divides the voltage it collects to measure the electrical potential difference in DC circuit and low-voltage, low-frequency AC circuit.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0002 | Voltage Sensor |  |
| 2 |  | Red alligator clip |  |
| 3 |  | Black alligator clip |  |

Usage

Connect Voltage Sensor to any port in SenseDisc.

Connect red and black alligator clips to positive and negative poles in Voltage Sensor.

Parallel connect Voltage Sensor into circuit.

Calibration

Voltage Sensor needs to be calibrated before using.

Short connect red and black alligator clips.

Open experiment software . Click  and select ‘Voltage Sensor’. Click ‘Calibrate’ ‘OK’ to complete calibration.

Typical experiment

Electromagnetic induction phenomenon

Primary cell experiment

Notes

Voltage Sensor should be parallel connected to the circuit during using.

Voltage Sensor needs to be calibrated before using.

The maximum voltage can be applied to sensor is 5V.

# Text boxes

S0002 Voltage Sensor

Measuring range: -500~500mV

Accuracy: ±1%

Resolution: 0.3mV

Input impedance: 500kΩ