Micro-Voltage Sensor

The Micro-Voltage Sensor is used to measure voltage within -60mV to 60mV. It amplifies the input voltage in order to measure voltage in micro level.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0004 | Micro-Voltage Sensor |  |
| 2 |  | Red alligator clip |  |
| 3 |  | Black alligator clip |  |

Usage

Connect Micro-Voltage Sensor to any port in SenseDisc.

Connect red and black alligator clips to positive and negative poles in Micro-Voltage sensor.

Parallel connect Micro-Voltage Sensor into circuit.

Calibration

Micro-Voltage Sensor needs to be calibrated before using.

Short connect red and black alligator clips.

Open experiment software . Click  and select ‘Micro-Voltage Sensor’. Click ‘Calibrate’ ‘OK’ to complete calibration.

Typical experiment

Charging and discharging for capacitor.

Notes

Micro-Voltage Sensor should be parallel connected to the circuit during using.

Micro-Voltage Sensor needs to be calibrated before using.

The maximum voltage can be applied to sensor is 500mV.

# Text boxes

S0004 Micro-Voltage Sensor

Measuring range: -60~60mV

Accuracy: ±1%

Resolution: 0.3mV

Input impedance: 1MΩ