# Current Sensor

Current Sensor is used to measure the current within 10uA in circuit. When current passes through resistor, it will form a tiny electric potential difference at both ends of the resistor. After circuit amplifying, it can accurately measure the current in circuit.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0006 | Current Sensor |  |
| 2 |  | Red alligator clip |  |
| 3 |  | Black alligator clip |  |

Usage

Connect Current Sensor to any port in SenseDisc.

Connect red and black alligator clips to positive and negative poles in Current Sensor.

Series connect Current Sensor into circuit.

Calibration

Current Sensor needs to be calibrated before using.

Short connect red and black alligator clips.

Open experiment software . Click  and select ‘Current Sensor’. Click ‘Calibrate’ ‘OK’ to complete calibration.

Typical experiment

Demonstration of power generation from human body

Electromagnetic induction phenomenon

Geomagnetic field generator

Thermoelectric current phenomenon

Photoelectric effect

Notes

Current Sensor should be series connected to circuit.

Current Sensor needs to be calibrated before using.

The maximum current can be applied to sensor is 100uA.

# Text boxes

S0006 Current Sensor

Measuring range: -10~10uA

Accuracy: ±1%

Resolution: 0.01uA

Internal resistance: 301Ω