# Milli-Current Sensor

Milli-Current Sensor is used to measure the current within -20 to 20mA in circuit. When current passes through resistor, it will form a tiny electric potential difference at both ends of the resistor. After circuit amplifying, it can accurately measure the current in circuit.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0007 | Milli-Current Sensor |  |
| 2 |  | Red alligator clip |  |
| 3 |  | Black alligator clip |  |

Usage

Connect Milli-Current Sensor to any port in SenseDisc.

Connect red and black alligator clips to positive and negative poles in Milli-Current Sensor.

Series connect Milli-Current Sensor into circuit.

Calibration

Milli-Current Sensor needs to be calibrated before using.

Short connect red and black alligator clips.

Open experiment software . Click  and select ‘Milli-Current Sensor’. Click ‘Calibrate’ ‘OK’ to complete calibration.

Typical experiment

Charging and discharging for capacitor.

Notes

Milli-Current Sensor should be series connected to circuit.

Milli-Current Sensor needs to be calibrated before using.

The maximum current can be applied to sensor is 100mA.

# Text boxes

S0007 Milli-Current Sensor

Measuring range: -20~20mA

Accuracy: ±1%

Resolution: 0.01mA

Internal resistance: 0.22Ω