# Temperature Sensor

Temperature Sensor is designed with NTC electronic element. When ambient temperature changes, resistance of NTC will also change. The sensor does not require calibration and it is relative high stable. The sensor is widely used in measuring temperature within medium and low range.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0009 | Temperature Sensor |  |
| 2 |  | Sensor Probe |  |

Usage

Connect Temperature Sensor to any port in SenseDisc.

Connect the sensor probe to Temperature Sensor.

Typical experiment

Natural cooling of water.

Liquid cooling via evaporation.

Conversion between work and energy.

Explore relationship between boiling point and pressure of liquid.

Acid-base neutralization reaction heat.

Comparison on heat conduction performance of different substances.

Seed germination.

Water solidification and ice melting.

Explore specific heat capacity.

Notes

Never place the sensor probe on or in open fire or heating disc directly.

Never immerse other parts of the Temperature Sensor other than its stainless steel bar into liquid when measuring its temperature.

Clean the Temperature Sensor completely after using.

Never place the sensor probe in the environment that temperature beyond measuring range.

# Text boxes

S0009 Temperature Sensor

Measuring range: -40~135℃

Accuracy: ±0.6℃

Resolution: 0.1℃