# Force Sensor

The sensing component of Force Sensor is a resistance strain gauge. It is attached to the metallic cross girder. It measures the force from two directions when the cross girder is deformed. The sensor converts force signal into voltage signal via resistance strain gauge. After circuit amplifying, it can accurately measure force value.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S3000 | Universal input |  |
| 2 | S0014 | Force Sensor |  |
| 3 |  | Hand screw |  |

Usage

Connect Force Sensor to universal input. Connect universal input to any port in SenseDisc.

Force Sensor can measure both pulling force and pressure. When pulling force is applied, it shows positive value. When pressure is applied, it shows negative value.

Calibration

Force Sensor needs to be calibrated before using.

Fix the hook on Force Sensor by screwing tightly.

Place the Force Sensor in a direction same as the measured force (for example: place it horizontal if you need to measure force which is horizontal ).

Open experiment software . Click  and select ‘Force Sensor’. Click ‘Calibrate’ ‘OK’ to complete calibration.

Typical experiment

Explore the Hooke’s law.

Newton’s third law.

Overweight and weightlessness.

Explore the simple harmonic motion.

Buoyancy law

Notes

Force Sensor needs to be calibrated before using.

Keep the direction of measured force vertical to the front panel of sensor to ensure the accuracy.

Please keep the force applied to the sensor not exceeding measuring range during measuring. Otherwise it may damage the Force Sensor.

Do not screw the hook too deep. Otherwise it will affect the accuracy.

# Text boxes

S0014 Force Sensor

Measuring range: -50~50N

Accuracy: ±1%

Resolution: 0.03N