# Motion Sensor

Motion sensor is a sonar equipment generating ultrasonic wave. It receives signal via signal reflecting by objects to measure the time T that high frequency sound wave pulse comes from object to sensor. According to the sound speed in air V, calculate distance between object and sensor: d=V*T/2.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0015 | Motion Sensor |  |

Usage

Connect Motion Sensor to any port in SenseDisc.

Aim the ultrasonic wave probe to object.

Place the object within the measuring range of Motion Sensor.

Typical experiment

Explore the simple harmonic motion

Forced vibration

Explore uniform linear motion and uniform accelerated motion

Notes

Be aware of the dead zone of Motion Sensor.

Keep the reflection surface of the object face to the sensor. The target surface should be big enough to ensure measuring accuracy.

Try to avoid sound interruption, because Motion Sensor only senses object near to it and has strong reflection.

# Text boxes

S0015 Motion Sensor

Measuring range: 20~600cm

Accuracy: ±2%

Resolution: 0.1cm