Radiation Monitor

S0022 Radiation Monitor is used to study radioactivity experiment. It is mainly used to measure intensity of γ-ray and β-ray.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S0022 | Radiation Monitor |  |
| 2 |  | Radiation Monitor Probe |  |

Usage

Radiation Monitor is not complicated. It is only required to connect all relative device. The Radiation Monitor probe tube wall is very thin. Be careful when using it, do not knock on the probe in case damage it.

Typical experiment

Measure radioactive source count rate

Measure background counting rate

Radioactive shield

Study relationship between radioactive intensity and distance

Measure radioactivity of building materials.

Notes

Do not knock on probe otherwise it will be broken easily.

Although the radioactive source used in school is normally weak, you still have to be careful with it.

Use pliers or other fixture to operate radioactive source. Do not place it near yourself or others.

Clean your hands after experiment.

Preserve the radioactive source properly. Lock and tag it.

# Text boxes

S0022 Radiation Monitor

Measuring range: 0 ~ 40000c/min

Accuracy: ±2%F.S

Resolution: 1c/min