# CO2 Sensor

CO2 Sensor is infrared gas absorption and testing sensor. It has good selectivity, high sensitivity, oxygen free dependent, long service life, low power consumption and no preheating requirement.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S3000 | Universal input |  |
| 2 | S1007 | CO2 Sensor |  |

Usage

Connect universal input to any port in SenseDisc.

Connect CO2 Sensor to universal input.

Place the sensor into the environment to be measured to collect data. Data display will be delay for 3~5 seconds.

Calibration

The sensor has been calibrated after manufacturing. Normally users can use it directly.

Due to long-term continuously use, the CO2 Sensor’s measuring value may have deviation. You can calibrate it when obvious error occurs. The method is shown below:

Wait until the output concentration of the testing sensor in the flowing air is stable (wait for about 5 minutes). Use pinpoint hold against the sensor reset button for 5 seconds. Generally, reset is not required.

Typical experiment

Plant's photosynthesis

Explore breathing regulation of saccharomycetes

Assessment of air quality

Generation velocity of CO2 in chemical reaction

Compare gas exhaled by human with the environmental gas

Notes

Try not to impact testing result by exhaled CO2.

If liquid flows into the probe, it will destroy the sensor completely.

Try not to use the sensor under condition which is full of dust.

CO2 is heavier than air so that it will sink to bottom of bottle. Use container as small as possible when doing experiment because it will be easier to collect CO2.

# Text boxes

S1007 CO2 Sensor

Measuring range: 0～100000ppm

Accuracy: (0~5000ppm) 3%;

(5000~50000ppm) 4%;

(50000~100000ppm) 6%;

Resolution: 2ppm