# UV Sensor

UV Sensor is used to detect UV light. The wavelength of UV light in electromagnetic spectrum is in the range of 100nm—400nm. The sensor is able to convert the UV light to voltage signal which is direct proportional to the strength of UV light.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S1040 | UV Sensor |  |

Usage

Connect UV Sensor to any port in SenseDisc.

Expose UV Sensor electrode in the environment to be measured.

Typical experiment

Detect the strength of local UV light.

The effect of UV light with different strength to biological survival rate.

Notes

Place UV Sensor under UV light during experiment. Do not look at UV light without protection.

Adjust the experiment time and acquisition interval of sensor via experiment software.

# Text boxes

S1040 UV Sensor

Measuring range: 0~400 W/m2

Accuracy: ±5%

Resolution: 0.1W/m2