# Introduction:

Sound Sensor not only can measure the intensity of sound (dB) within two measuring ranges, but also be used to measure the wave form (mV) of sound directly. The response frequency range of Sound Sensor is 20Hz～20kHz, which has very short response time. It is able to capture sound speed and sound wave.

Sound Sensor collects sound signal using electret microphone. It is able to differ sound level and frequency. The red button on Sound Sensor is used to shift the measuring range. Press the button and the measuring range will become 80dB～120dB. Otherwise it will be 30dB～90dB. At the same time, electret microphone converts sound vibration signal to voltage signal and output to computer by amplifying circuit.

Calibration:

Calibration is not required.

Usage:

Sound Sensor is a kind of special sensor. There is a specific software designed for it. You can click ‘New’ (for sound level) or ‘Sound’ (for sound wave) according to your requirement.

Typical experiment:

- Measure the grade of sound intensity

- Measure the strength of noise

- Measure the speed of sound in the air

- Synthesis of sound wave

- Synthesis of sound composition

Experimental case:

Synthesis of sound composition

Product General Assembly

Experimental procedures：

1. Connect experiment apparatus.

2. Open SWR iLab v8.0.

3. Click ‘Sound’ and set proper experimental time.

4. Click ‘Start’ after knocking two tune forks using mallet.

5. Analyze the experimental result after collecting.

6. Select a certain zone and click ‘FFT’ to get frequency curve.

7. Observe and analyze the frequency curve.

8. Clear up experimental apparatus.

Sound Composition

FFT Sound

Notes:

1. Sound Sensor must be used with ‘Sound’ in SWR iLab.

2. Please make sure the sound to be measured within the range. If it exceeds measuring range, keep the sensor away from it or decrease sound level.

3. The Sound Sensor is not waterproof. If use the sensor in a wet environment, try to prevent water flowing into sensor.

# Text boxes

Sound Sensor

Product No.: TS2112

Sound level:

Low range: 30dB～90dB

Resolution: 0.1dB

Accuracy: ±2dB

High range: 80dB～120dB

Resolution: 0.1dB

Accuracy: ±2dB

Address: No.14 Junnong Road, Qinhuai District, Nanjing, China.

Website: //www.sinoswr.com

Post Code: 210007

Tel: +86-400-828-8387