Introduction:

The sensing component in Three Range Light Sensor is silicon photocell. It is able to transfer light intensity to voltage signal which is direct proportional to it. The valid spectrum wavelength of Three Range Light Sensor is 380nm~730nm, which is ideal visible light section.

The sensing component of Three Range Light Sensor is placed in the front end of probe. Aim the light receiving area to the light beam during using.

There is a switch on Three Range Light Sensor is used to shift the measuring range. The measuring range of sensor are 0～600Lux, 0～6000Lux and 0～50000Lux.

Calibration:

Calibration is not required.

Usage:

The usage of Three Range Light Sensor is simple. Connect Three Range Light Sensor to datalogger and datalogger to computer. Open relative software to measure the light. Be careful when selecting measuring range.

Typical experiment:

Explore the relationship between illumination and distance

Explore the diffraction, interference and polarization of light

Explore illumination affecting the rate of photosynthesis

Experimental case:

Explore the relationship between illumination and distance

Product General Assembly

Experimental procedures：

1. Connect experiment apparatus.

2. Open SWR iLab v8.0. Click ‘New’ to create new experimental template. Click ‘New page’ and select the sixth template to create new folder.

3. Click ‘add line’ to add ‘Light-Distance’ coordinate. Click ‘list select’ at upper left corner. Set proper collecting time and acquisition interval such as 1min, 100ms.

4. Put the Three Range Light Sensor 5cm away from the point light source.

5. Click the ‘Manually’ button to collect the experimental data.

6. Move the Three Range Light Sensor 1 more cm away from the light source.

7. Repeat procedure 5 and 6 till enough data points are collected.

8. Click ‘Stop’ button to complete data acquisition.

9. Analyze the experimental result

10. Clear up experimental apparatus.

Illumination-Distance Curve

Notes:

1. Keep the probe aiming to the light source when using it.

2. Select the proper measuring range when measuring in order to ensure the accuracy of experimental result.

# Text boxes

Address: No.14 Junnong Road, Qinhuai District, Nanjing, China.

Website: //www.sinoswr.com

Post Code: 210007

Tel: +86-400-828-8387

Three Range Light Sensor

Product No.: TS2122

Low range: 0～600Lux

Resolution: 0.15Lux

Accuracy: ±5%

Medium range: 0～6000Lux

Resolution: 1.5Lux

Accuracy: ±5%

High range: ～150000Lux

Resolution: 38Lux

Accuracy: ±5%