Introduction:

Dissolved CO2 Sensor is used to detect concentration of CO2 in solution. It can measure the concentration using datalogger and experiment software. The dissolved CO2 in sample diffuses in the thin liquid layer between pH electrode and gas-permeable membrane. The reaction will occur until partial pressure of sample and thin liquid layer are same.

CO2+H2O     H++HCO3-

The change of pH of thin liquid layer is measured by combination electrode. The measured potential value and concentration of CO2 in external solution are compliance with Nernst formula.

Usage:

1. Connect sensor to datalogger and datalogger to computer.

2. Open SWR iLab. The product has been calibrated before manufacturing. You can use it directly.

3. Immerse the probe into solution with dissolved CO2.

Typical experiment:

Solubleness of carbon dioxide

Absorb carbon dioxide by photosynthesis of aquatic plant

Notes:

Before experiment, make sure the position of gas-permeable membrane and pH electrode are placed properly. If they are touching too tight, the liquid layer maybe too thin to connect so that the potential will not be stable. If they are touching too separately, the time required to be stable will be too long.

After every time of using, rinse the electrode using deionized water to keep the potential at -450mV.

During experiment, it should start from dilute to concentrated solution. It should be carried out in small beaker without sealing. In order to prevent effusion of CO2, it is suggested to add acid and stir the solution after immersing electrode in solution and then start measuring data.

The internal resistance of apparatus using with electrode should have at least 3×1011Ω to make sure the electrode is insulated.

pH value range: 0-4.

Respond time: 1×10-2～1×10-4mol/L, less than 4minutes (25℃).

1×10-4～5×10-5mol/L, less than 7minutes (25℃).

Main interruption: NO2, SO2, HAC and CH2O.

# Text boxes

Address: No.14 Junnong Road, Qinhuai District, Nanjing, China.

Website: //www.sinoswr.com

Post Code: 210007

Tel: +86-400-828-8387

Dissolved CO2 Sensor

Product No.: TS2218

Measuring range: 0.2ppm～440ppm

Resolution: 0.1 ppm