| G-M Sensor ZC0022 Measuring range: 0~40000c/min Sensing component: The G-M component is installed in the black probe. Notes: It can be used once connected to related device. Do not hit or knock the probe. Otherwise it may damage it. The sensor must be working with external power supply. Thus, connect datalogger to power supply. Otherwise, probe will not work properly. | ZC0022 G-M Sensor is used to study radioactivity experiment. It is mainly used to measure intensity of γ-ray and β-ray. Data cable (USB interface) Datalogger Computer installed with SWR iLab v8.0 and above. 1. Connect the sensor to computer by USB cable. 2. Open the SWR iLab v8.0. 3. Click to create new experimental template. |
| --- | --- |

| Device status: The icon shows blue. It means that the sensor has been recognized by the software. Rapid experiment: Click thebutton. The system will automatically create the experimental template. Start: Click the button. The system will start collecting data. Stop: Click the button to stop data acquisition. Zone select: Click the button to select the data area need to be analyzed. | Measure background counting rate Radioactive shield Explore relationship between radioactive intensity and distance Connect the sensor to computer using USB cable. Connect sensor and datalogger using network cable. Open the SWR iLab v8.0. Click ‘Rapid experiment’. The system will create coordinate automatically. Set the acquisition time to 5 minutes and acquisition interval to 100ms. Move the sensor’s probe close to radiation source. Click ‘Start’ button. Click ‘Stop’ button data acquisition. Click ‘Zone select’ button. Select the data area and check the average measuring value, as shown in Fig.1 Fig.2 |
| --- | --- |
| This sensor needs no calibration or demarcation. | In ZC0022 G-M Sensor, the incident particles is only a trigger for discharging. Therefore, its output voltage pulse has nothing to do with the property and energy of the incident ion. G-M Sensor can not be used to measure the energy of the incident particle but only measure the quantity. |

# Text boxes

Product specification:

Address: No.14 Junnong Road, Qinhuai District, Nanjing, China

Website: //www.sinoswr.com      Post Code: 210007

Tel: +86-400-828-8387