| Heart Rate Sensor ZC1024 Measuring range: 40~160 BPM Sensing component: The measuring component is the metal piece on handle. Usage: The Heart Rate Sensor must be used independently with heart rate software. User should clench the red handle by left hand when measuring. Clench the black handle by the right hand. Attach the metal piece to your hand tightly. The reading value is available only after 9s since measuring starting. | ZC1024 Heart Rate Sensor is used to measure the heart rate of human body. Data cable Computer installed with SWR iLab v8.0 and above. The sensor red and black cylindrical handles are connected using a spiral wire. The black handle is connected to the computer using a cable with Mini USB interface. Open the SWR iLab V8.0. Click the ‘Heart rate’ button to enter into the experiment template. |
| --- | --- |

| Device status: The icon shows blue. It means that the sensor has been recognized by the software. Start: Click the button. The system will start collecting data. Stop: Click the button to stop data acquisition. | Measure the heart rate of human body Connect the sensor to datalogger using cable and datalogger to computer using USB cable. Open the heart rate software and enter into experiment template. Click the ‘Start’ button. User should clench the red handle by left hand and the black handle by right hand. Attach the metal piece tightly to your hand. After about 9 seconds, it can be seen that the heart rate value will be basically stable at an exact number. Record the value. |
| --- | --- |
| This sensor needs no calibration or demarcation. | The sensing element of ZC1024 Heart Rate Sensor is a metal patch. It can be reused without replacement which is convenient to measure. |

# Text boxes

Product specification:

Address: No.14 Junnong Road, Qinhuai District, Nanjing, China

Website: //www.sinoswr.com      Post Code: 210007

Tel: +86-400-828-8387