# EKG Sensor

EKG Sensor is used detect the micro voltage produced by heartbeat. Two wires are used to measure the change of voltage and convert them into electric signal. The change of voltage is displayed in wave form.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S1011 | EKG Sensor |  |
| 2 |  | Electrode patches |  |
| 3 |  | Wires |  |

Usage

Connect universal input to any port in SenseDisc.

Connect wires to sensor.

Buckle 3 electrode patches on wires. Attach them on the corresponding position on your body as shown in figure

Typical experiment

Measure the human electrocardiogram

Notes

This product is designed to certify EKG wave form but can not be used for medical diagnosis. Information produced by most signals is pointless to any medical purpose.

If the electrode pack is opened, please keep it in a dry and cool place.

Attach the electrode patch at correct position.

The power source should be grounded during using.

# Text boxes

S1011 EKG Sensor

Measuring range: -1mV~5mV

Resolution: 0.0025mV