SO2 Sensor

The working principle of SO2 Sensor is electrochemistry. When SO2 gets inside of electrode, electrical potential and current will be generated according to the working principle. Sensor collects those data and display the concentration of SO2 according to the relationship between SO2 and electrical potential and current.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S1014 | SO2 Sensor |  |
| 2 |  | SO2 Sensor electrode |  |

Usage

Connect SO2 Sensor to any port in SenseDisc.

Connect electrode to SO2 Sensor.

Preserve the electrode at proper place after using.

Typical experiment

Assessment of air quality

Detect automobile exhaust

Measure SO2 in chemical reaction

Notes

Do not touch it to liquid or other organic matter. Use and preserve it in dry place. Otherwise, those matters could damage the electrode.

SO2 Sensor electrode has limited service life according to its working principle.

Data display will be delay due to electrochemistry.

Do not use and preserve it in high concentration alkali gas.

# Text boxes

S1014 SO2 Sensor

Measuring range: 0~ 20ppm

Accuracy: ±1%F.S

Resolution: 0.1ppm