CO Sensor

CO Sensor is a kind of constant potential electrolytic type sensor. CO and O2 produce charge and form current by redox reaction. The amplitude of current is direct proportional to concentration of CO. We can determine the concentration of CO is high or low by detecting current.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S1027 | CO Sensor |  |
| 2 |  | CO Sensor electrode |  |

Usage

Connect CO Sensor to any port in SenseDisc.

Expose CO Sensor electrode in the air with CO to collect data.

Typical experiment

Produce CO using concentrated sulfuric acid.

Detect concentration of CO when coal inadequate combustion.

Notes

Do not touch it to liquid or other organic matter. Use and preserve it in dry place. Otherwise, those matters could damage the electrode.

CO Sensor electrode has limited service life according to its working principle.

Data display will be delay due to electrochemistry.

CO is kind of flammable and combustible gas. It can form explosive mixture with air and explode when it meets open fire or high temperature. The explosion limitation of CO and gas mixture is 12%～75%.

The CO Sensor electrode is gas-permeable membrane electrode. Try not to break the membrane during using.

# Text boxes

S1027 CO Sensor

Measuring range: 0 ~ 1000ppm

Accuracy: ±1%F.S

Resolution: 1ppm