# O3 Sensor

The working principle of O3 Sensor is measuring concentration of gas by using electrochemistry. The probe consists of electrode and electrolyte. The electrolyte is separated by a selective gas-permeable membrane. The gas diffusing in sensor occurs redox reaction on the surface of electrode. Current is generated in the electrode. The value of current is corresponding to the concentration of gas. Sensor converts the signal in electrode into analog signal.

Component

| No. | Model | Name | Picture |
| --- | --- | --- | --- |
| 1 | S1030 | O3 Sensor |  |
| 2 |  | O3 Sensor electrode |  |

Usage

Connect O3 Sensor to any port in SenseDisc.

Connect electrode to O3 Sensor.

Place O3 Sensor in the environment to be measured to collect data.

Typical experiment

Detect concentration of O3 in water

Detect concentration of O3 in air

Notes

The electrode is gas-permeable membrane electrode. Try not to break the membrane when assembling the device.

During using, wait until the reading becomes stable. Take out the electrode from solution and rinse it using distilled water. Dry it using filter paper and cover it.

Do not wipe the electrode using cleanser or gauze. It may damage the cover.

Take precautions when dealing with water or solution with O3.

# Text boxes

S1030 O3 Sensor

Measuring range: 0～20ppm

Accuracy: ±1%F.S

Resolution: 0.02ppm